White Paper		 		                    NEAL NELSON & ASSOCIATES

Throughput and Power Efficiency

for

AMD and Intel Quad Core

Processors

January 14, 2008

Copyright © 2008, Neal Nelson & Associates

# 1. Management Summary

Tests of servers using Intel and AMD quad core processors showed that the Intel based servers delivered slightly better maximum throughput and the Opteron based servers were substantially more power efficient. More specifically:

- When the sizes of the database working sets were small enough to fit in the servers’ kernel disk buffer cache, so that there was virtually no physical disk I/O, the Xeon based servers delivered up to 14 percent higher throughput than the Opteron based servers.

- When the sizes of the database working sets were too large to fit in the kernel disk buffer cache, which forced substantial physical disk I/O, the Xeon based servers delivered up to 3 percent higher throughput than the Opteron based servers

- When the servers were subjected to various identical levels of transaction arrival rates the Opteron based servers consumed up to 32 percent less power than the Xeon based servers.

- When the systems were idle and waiting for transactions to process the Opteron based servers consumed up to 41 percent less power than the Xeon based servers.

The power consumption at idle is particularly significant since studies have shown that many servers are powered on, but idle, 80 percent of the time. (1) (2)

Finally there was a comparison of a 2.0 GHz Xeon to a 2.33 GHz Xeon which showed that although the 2.33 GHz chip had a 16 percent faster clock speed, the range of throughput increase was 6 to 10 percent in the cached domain and 0.1 to 2.2 percent when physical disk I/O was taking place.

There is a consensus in the industry that a substantial amount of a Xeon server’s power usage can be traced to Intel’s use of fully buffered memory modules (FB-DIMMs).  The expectation is that for systems with a larger number of DIMMs AMD based servers will have a significant power consumption advantage.  For systems with a smaller number of DIMMs the power consumption advantage might shift to Intel.  All of the tests in this paper were run with 1 gigabyte memory modules.  Future tests may be performed with 2 or 4 gigabyte modules.

These tests were run with a complex workload that included physical disk I/O, substantial network traffic, applications with a large memory footprint and a significant level of context switches.

As a computer consultant with over 35 years experience, Neal Nelson offers his customers a money-back guarantee for a high level of correlation between predictions based on this test methodology and the customers’ real world experiences.

# 2. Test Objective

The objective for this test was to compare the throughput and power efficiency of servers that use AMD Opteron quad core processors to servers that use the Intel Xeon quad core processors.

# 3. Comparing These Test Results to Results from SPECPower.

Some of the test results in this paper differ with test results recently published by the SPEC committee.  These differences are easy to understand if one looks at the differences between the Neal Nelson Power Efficiency Test and the SPECPower test.  The following table lists some areas where there are differences between the two tests.

| Characteristic | Neal Nelson Power Efficiency Test | SPECPower Benchmark |
| --- | --- | --- |
| Application Software | Apache2, “C” Programs | Proprietary Java Application(3) |
| Application Memory Footprint | Large, Complex | Small, Simple |
| Test Database Size | Larger (approx. 140 GB) | Smaller(5) |
| Location of Data Tables | Disk | Memory(5) |
| Disk Input/Output During Test | Yes | No(5) |
| Database Management | MySQL, Oracle, Sybase, etc. | Undocumented |
| Access to Data Tables | Structured Query Language | Undocumented |
| Record Locking | Yes (50% of all transactions) | No(5) |
| No. Trans. Per Screen/Batch | 1 | 1,000(4) |
| Max. Simultaneous “Users” | 500 | Typically 1,2,4 |
| No. of “Client” Computers | 32 | 1 |
| Network Traffic During Test | Complex | Simple |
| Operating System | Always Suse Linux Ent. Server | Varies |
| Operating System Tunables | Always Identical | Varies |

Figure 1:  Differences, Neal Nelson Power Efficiency Test and the SPECPower Benchmark

With all of these differences in configuration and workload there should be no surprise that the benchmarks yield different results.

A review of these differences shows clearly that users with a single client machine accessing a small Java application processing groups of 1,000 transactions per batch to data tables that are kept in memory tables with no physical disk I/O should favor the SPECPower Benchmark.  Users that have many client computers with many active users accessing applications like Apache2 and DBMS packages like MySQL, Oracle or Sybase with larger data tables that are stored on disk drives should favor the Neal Nelson test.

# 4. One Socket 2.0 GHz Quad Xeon vs. 2.0 GHz Quad Opteron

The first set of test data compares the throughput and power efficiency of a single socket 2.0 GHz Xeon to a 2.0 GHz Opteron.  Note that at the lower user counts the database working set resides in the kernel disk buffer cache so there is almost no physical disk I/O.  As the user count increases the database working set overflows the kernel cache and the test becomes limited by the speed of the disk sub-system.

| 2 GHz Xeon vs. 2 Ghz Opteron, 4 GB, 1 GB DIMMs |
| --- |
| Data Collected During 30 Min. Trans. Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | Xeon | Opteron |  |  |
| 100 | 13,996 | 13,858 | 1.0 | Xeon |
| 150 | 14,839 | 14,536 | 2.1 | Xeon |
| 200 | 7,641 | 7,300 | 4.7 | Xeon |
| 250 | 4,879 | 4,971 | 1.9 | Opteron |
| 300 | 5,050 | 5,019 | 0.6 | Xeon |
| 350 | 5,339 | 5,241 | 1.9 | Xeon |
| 400 | 5,324 | 5,263 | 1.2 | Xeon |
| 450 | 5,392 | 5,331 | 1.1 | Xeon |
| 500 | 5,241 | 5,233 | 0.2 | Xeon |

Figure 2:  Throughput, One Socket, 2.0 GHz Xeon vs. 2.0 GHz Opteron, 4 –1 GB DIMMs

| 2 GHz Xeon vs. 2 Ghz Opteron, 8 GB, 1 GB DIMMs |
| --- |
| Data Collected During 30 Min. Trans. Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | Xeon | Opteron |  |  |
| 100 | 14,015 | 13,787 | 1.7 | Xeon |
| 150 | 14,800 | 14,440 | 2.5 | Xeon |
| 200 | 11,976 | 11,458 | 4.5 | Xeon |
| 250 | 6,415 | 6,346 | 1.1 | Xeon |
| 300 | 6,313 | 6,276 | 0.6 | Xeon |
| 350 | 5,921 | 5,882 | 0.7 | Xeon |
| 400 | 5,461 | 5,462 | 0.0 | Opteron |
| 450 | 5,443 | 5,375 | 1.3 | Xeon |
| 500 | 5,478 | 5,421 | 1.1 | Xeon |

Figure 3:  Throughput, One Socket, 2.0 GHz Xeon vs. 2.0 GHz Opteron, 8 –1 GB DIMMs

The next two tables show power efficiency comparisons at two different memory sizes when the 2.0 GHz Xeon and 2.0 GHz Opteron are subjected to identical transaction arrival rates.

| 1 Socket, 2.0 GHz Xeon vs. 2.0 GHz Opteron, 4 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | Xeon | Opteron | Xeon | Opteron |  |  |
| Idle |  |  | 172.8 | 130.4 | 24.5 | Opteron |
| 100 | 2,407 | 2,406 | 179.4 | 146.4 | 18.4 | Opteron |
| 200 | 4,814 | 4,812 | 186.8 | 156.4 | 16.3 | Opteron |
| 300 | 7,221 | 7,221 | 192.6 | 165.4 | 14.1 | Opteron |
| 400 | 9,625 | 9,628 | 198.6 | 172.8 | 13.0 | Opteron |
| 500 | 12,030 | 12,033 | 202.6 | 176.0 | 13.1 | Opteron |

Figure 4:  Power Efficiency, One Socket, 2.0 GHz Xeon vs. 2.0 GHz Opteron, 4 –1 GB DIMMs

| 1 Socket, 2.0 GHz Xeon vs. 2.0 GHz Opteron, 8 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | Xeon | Opteron | Xeon | Opteron |  |  |
| Idle |  |  | 207.6 | 134.4 | 35.3 | Opteron |
| 100 | 2,406 | 2,407 | 220.8 | 152.4 | 31.0 | Opteron |
| 200 | 4,814 | 4,813 | 219.6 | 162.8 | 25.9 | Opteron |
| 300 | 7,221 | 7,221 | 225.4 | 172.4 | 23.5 | Opteron |
| 400 | 9,628 | 9,624 | 230.4 | 180.0 | 21.9 | Opteron |
| 500 | 12,031 | 12,028 | 234.6 | 183.2 | 21.9 | Opteron |

Figure 5:  Power Efficiency, One Socket, 2.0 GHz Xeon vs. 2.0 GHz Opteron, 8 –1 GB DIMMs

# 5. One Socket 2.33 GHz Quad Xeon vs. 2.0 GHz Quad Opteron

The second set of test data compares the throughput and power efficiency of a single socket 2.33 GHz Xeon to a 2.0 GHz Opteron.  Note that at the lower user counts the database working set resides in the kernel disk buffer cache so there is almost no physical disk I/O.  As the user count increases the database working set overflows the kernel cache and the test becomes limited by the speed of the disk sub-system.

| 2.33 GHz Xeon vs. 2.0 Ghz Opteron, 4 GB, 1 GB DIMMs |
| --- |
| Data Collected During 30 Min. Trans. Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | Xeon | Opteron |  |  |
| 100 | 15,121 | 13,858 | 9.1 | Xeon |
| 150 | 15,846 | 14,536 | 9.0 | Xeon |
| 200 | 7,603 | 7,300 | 4.2 | Xeon |
| 250 | 5,071 | 4,971 | 2.0 | Xeon |
| 300 | 5,080 | 5,019 | 1.2 | Xeon |
| 350 | 5,342 | 5,241 | 1.9 | Xeon |
| 400 | 5,373 | 5,263 | 2.1 | Xeon |
| 450 | 5,395 | 5,331 | 1.2 | Xeon |
| 500 | 5,268 | 5,233 | 0.7 | Xeon |

Figure 6:  Throughput, One Socket, 2.33 GHz Xeon vs. 2.0 GHz Opteron, 4 –1 GB DIMMs

| 2.33 GHz Xeon vs. 2.0 Ghz Opteron, 8 GB, 1 GB DIMMs |
| --- |
| Data Collected During 30 Min. Trans. Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | Xeon | Opteron |  |  |
| 100 | 14,857 | 13,787 | 7.8 | Xeon |
| 150 | 15,851 | 14,440 | 9.8 | Xeon |
| 200 | 13,021 | 11,458 | 13.6 | Xeon |
| 250 | 6,459 | 6,346 | 1.8 | Xeon |
| 300 | 6,284 | 6,276 | 0.1 | Xeon |
| 350 | 5,950 | 5,882 | 1.2 | Xeon |
| 400 | 5,476 | 5,462 | 0.3 | Xeon |
| 450 | 5,459 | 5,375 | 1.6 | Xeon |
| 500 | 5,495 | 5,421 | 1.4 | Xeon |

Figure 7:  Throughput, One Socket, 2.33 GHz Xeon vs. 2.0 GHz Opteron, 8 –1 GB DIMMs

The next two tables show power efficiency comparisons at two different memory sizes when the 2.33 GHz Xeon and 2.0 GHz Opteron were subjected to identical transaction arrival rates.

| 1 Socket, 2.33 GHz Xeon vs. 2.0 GHz Opteron, 4 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | Xeon | Opteron | Xeon | Opteron |  |  |
| Idle |  |  | 172.6 | 130.4 | 24.4 | Opteron |
| 100 | 2,406 | 2,406 | 179.4 | 146.4 | 18.4 | Opteron |
| 200 | 4,812 | 4,812 | 186.0 | 156.4 | 15.9 | Opteron |
| 300 | 7,219 | 7,221 | 192.0 | 165.4 | 13.9 | Opteron |
| 400 | 9,627 | 9,628 | 197.2 | 172.8 | 12.4 | Opteron |
| 500 | 12,034 | 12,033 | 202.2 | 176.0 | 13.0 | Opteron |

Figure 8:  Power Efficiency, One Socket, 2.33 GHz Xeon vs. 2.0 GHz Opteron, 4 –1 GB DIMMs

| 1 Socket, 2.33 GHz Xeon vs. 2.0 GHz Opteron, 8 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | Xeon | Opteron | Xeon | Opteron |  |  |
| Idle |  |  | 204.6 | 134.4 | 34.3 | Opteron |
| 100 | 2,406 | 2,407 | 212.6 | 152.4 | 28.3 | Opteron |
| 200 | 4,813 | 4,813 | 220.8 | 162.8 | 26.3 | Opteron |
| 300 | 7,220 | 7,221 | 224.4 | 172.4 | 23.2 | Opteron |
| 400 | 9,629 | 9,624 | 229.8 | 180.0 | 21.7 | Opteron |
| 500 | 12,031 | 12,028 | 233.8 | 183.2 | 21.6 | Opteron |

Figure 9:  Power Efficiency, One Socket, 2.33 GHz Xeon vs. 2.0 GHz Opteron, 8 –1 GB DIMMs

# 6. Two Sockets 2.33 GHz Quad Xeons vs. 2.0 GHz Quad Opterons

The third set of test data compares the throughput and power efficiency of servers with two 2.33 GHz Xeons and two 2.0 GHz Opterons.  Note that at the lower user counts the database working set resides in the kernel disk buffer cache so there is almost no physical disk I/O.  As the user count increases the database working set overflows the kernel cache and the test becomes limited by the speed of the disk sub-system.

| 2 Sockets, 2.33 GHz Xeons vs. 2.0 Ghz Opterons, 4 GB |
| --- |
| Data Collected During 30 Min. Transaction Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | Xeon | Opteron |  |  |
| 100 | 19,772 | 19,180 | 3.1 | Xeon |
| 150 | 22,389 | 20,729 | 8.0 | Xeon |
| 200 | 7,896 | 7,878 | 0.2 | Xeon |
| 250 | 5,179 | 5,049 | 2.6 | Xeon |
| 300 | 5,218 | 5,077 | 2.8 | Xeon |
| 350 | 5,436 | 5,304 | 2.5 | Xeon |
| 400 | 5,453 | 5,332 | 2.3 | Xeon |
| 450 | 5,396 | 5,384 | 0.2 | Xeon |
| 500 | 5,343 | 5,310 | 0.6 | Xeon |

Figure 10:  Throughput, Two Sockets, 2.33 GHz Xeons vs. 2.0 GHz Opterons, 4 –1 GB DIMMs

| 2 Sockets, 2.33 GHz Xeons vs. 2.0 Ghz Opterons, 8 GB |
| --- |
| Data Collected During 30 Min. Transaction Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | Xeon | Opteron |  |  |
| 100 | 20,030 | 19,390 | 3.3 | Xeon |
| 150 | 22,618 | 20,739 | 9.1 | Xeon |
| 200 | 18,302 | 16,841 | 8.7 | Xeon |
| 250 | 6,642 | 6,591 | 0.8 | Xeon |
| 300 | 6,552 | 6,469 | 1.3 | Xeon |
| 350 | 5,939 | 5,944 | 0.1 | Opteron |
| 400 | 5,521 | 5,481 | 0.7 | Xeon |
| 450 | 5,497 | 5,450 | 0.9 | Xeon |
| 500 | 5,493 | 5,484 | 0.2 | Xeon |

Figure 11:  Throughput, Two Sockets, 2.33 GHz Xeons vs. 2.0 GHz Opterons, 8 –1 GB DIMMs

| 2 Sockets, 2.33 GHz Xeons vs. 2.0 Ghz Opterons, 16 GB |
| --- |
| Data Collected During 30 Min. Transaction Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | Xeon | Opteron |  |  |
| 100 | 19,915 | 19,466 | 2.3 | Xeon |
| 150 | 22,557 | 20,576 | 9.6 | Xeon |
| 200 | 18,240 | 17,429 | 4.7 | Xeon |
| 250 | 7,296 | 7,181 | 1.6 | Xeon |
| 300 | 7,281 | 7,180 | 1.4 | Xeon |
| 350 | 7,483 | 7,412 | 1.0 | Xeon |
| 400 | 7,565 | 7,478 | 1.2 | Xeon |
| 450 | 7,583 | 7,503 | 1.1 | Xeon |
| 500 | 7,309 | 7,278 | 0.4 | Xeon |

Figure 12:  Throughput, Two Sockets, 2.33 GHz Xeons vs. 2.0 GHz Opterons, 16 –1 GB DIMMs

The next three tables show power efficiency comparisons at three different memory sizes when the 2.33 GHz Xeon and 2.0 GHz Opteron were subjected to identical transaction arrival rates.

| 2 Sockets, 2.33 GHz Xeons vs. 2.0 GHz Opterons, 4 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | Xeon | Opteron | Xeon | Opteron |  |  |
| Idle |  |  | 195.6 | 159.8 | 18.3 | Opteron |
| 100 | 2,406 | 2,407 | 203.6 | 189.8 | 6.8 | Opteron |
| 200 | 4,815 | 4,813 | 213.0 | 204.8 | 3.8 | Opteron |
| 300 | 7,221 | 7,218 | 220.2 | 218.0 | 1.0 | Opteron |
| 400 | 9,630 | 9,627 | 227.8 | 229.4 | 0.7 | Xeon |
| 500 | 12,032 | 12,036 | 241.8 | 239.0 | 1.2 | Opteron |

Figure 13:  Power Efficiency, Two Sockets, 2.33 GHz Xeons vs. 2.0 GHz Opterons, 4 –1 GB DIMMs

| 2 Sockets, 2.33 GHz Xeons vs. 2.0 GHz Opterons, 8 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | Xeon | Opteron | Xeon | Opteron |  |  |
| Idle |  |  | 227.2 | 163.8 | 27.9 | Opteron |
| 100 | 2,406 | 2,407 | 236.6 | 195.6 | 17.3 | Opteron |
| 200 | 4,813 | 4,813 | 245.2 | 210.2 | 14.3 | Opteron |
| 300 | 7,221 | 7,219 | 252.4 | 224.6 | 11.0 | Opteron |
| 400 | 9,628 | 9,625 | 259.8 | 236.6 | 8.9 | Opteron |
| 500 | 12,037 | 12,034 | 265.6 | 245.8 | 7.5 | Opteron |

Figure 14:  Power Efficiency, Two Sockets, 2.33 GHz Xeons vs. 2.0 GHz Opterons, 8 –1 GB DIMMs

| 2 Sockets, 2.33 GHz Xeons vs. 2.0 GHz Opterons, 16 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | Xeon | Opteron | Xeon | Opteron |  |  |
| Idle |  |  | 295.0 | 173.4 | 41.2 | Opteron |
| 100 | 2,407 | 2,407 | 303.8 | 206.0 | 32.2 | Opteron |
| 200 | 4,812 | 4,814 | 311.8 | 223.8 | 28.2 | Opteron |
| 300 | 7,221 | 7,220 | 319.4 | 240.0 | 24.9 | Opteron |
| 400 | 9,629 | 9,628 | 327.2 | 252.0 | 23.0 | Opteron |
| 500 | 12,036 | 12,036 | 333.0 | 262.0 | 21.3 | Opteron |

Figure 15:  Power Efficiency, Two Sockets, 2.33 GHz Xeons vs. 2.0 GHz Opterons, 16 –1 GB DIMMs

# 7. One Socket 2.0 GHz Quad Xeon vs. 2.33 GHz Quad Xeon

The last set of test data compares the throughput and power efficiency of a server with a single 2.0 GHz Xeon to the same server with a single 2.33 GHz Xeon.  At the lower user counts the database working set resides in the kernel disk buffer cache so there is essentially no physical disk I/O.  As the user count increases the database working set overflows the kernel cache and the test becomes limited by the speed of the disk sub-system.

It is interesting to note that the clock speed of the 2.33 GHz processor is 16 percent faster than the 2.0 GHz processor but that the maximum increase in throughput for cached I/O is 10 percent and the maximum increase in throughput for physical disk I/O is 2.2 percent.

| 2.0 GHz Versus 2.33 GHz Xeon, 4 GB, 1 GB DIMMs |
| --- |
| Data Collected During 30 Min. Trans. Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | 2.0 GHz | 2.33 GHz |  |  |
| 100 | 13,996 | 15,121 | 8.0 | 2.33 GHz |
| 150 | 14,839 | 15,846 | 6.8 | 2.33 GHz |
| 200 | 7,641 | 7,603 | 0.5 | 2.0 GHz |
| 250 | 4,879 | 5,071 | 3.9 | 2.33 GHz |
| 300 | 5,050 | 5,080 | 0.6 | 2.33 GHz |
| 350 | 5,339 | 5,342 | 0.1 | 2.33 GHz |
| 400 | 5,324 | 5,373 | 0.9 | 2.33 GHz |
| 450 | 5,392 | 5,395 | 0.1 | 2.33 GHz |
| 500 | 5,241 | 5,268 | 0.5 | 2.33 GHz |

Figure 16:  Throughput Comparison of 2.0 and 2.33 GHz Xeons with 4 GB of Memory

| 2.0 GHz Versus 2.33 GHz Xeon, 8 GB, 1 GB DIMMs |
| --- |
| Data Collected During 30 Min. Trans. Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | 2.0 GHz | 2.33 GHz |  |  |
| 100 | 14,015 | 14,857 | 6.0 | 2.33 GHz |
| 150 | 14,800 | 15,851 | 7.1 | 2.33 GHz |
| 200 | 11,976 | 13,021 | 8.7 | 2.33 GHz |
| 250 | 6,415 | 6,459 | 0.7 | 2.33 GHz |
| 300 | 6,313 | 6,284 | 0.5 | 2.0 GHz |
| 350 | 5,921 | 5,950 | 0.5 | 2.33 GHz |
| 400 | 5,461 | 5,476 | 0.3 | 2.33 GHz |
| 450 | 5,443 | 5,459 | 0.3 | 2.33 GHz |
| 500 | 5,478 | 5,495 | 0.3 | 2.33 GHz |

Figure 17:  Throughput Comparison of 2.0 and 2.33 GHz Xeons with 8 GB of Memory

| 2.0 GHz Versus 2.33 GHz Xeon, 16 GB, 1 GB DIMMs |
| --- |
| Data Collected During 30 Min. Trans. Processing Tests |
| Active Users | Transactions Per Min. | Percent Higher | Better Option |
|  | 2.0 GHz | 2.33 GHz |  |  |
| 100 | 13,810 | 14,928 | 8.1 | 2.33 GHz |
| 150 | 14,631 | 15,752 | 7.7 | 2.33 GHz |
| 200 | 11,736 | 12,907 | 10.0 | 2.33 GHz |
| 250 | 6,724 | 6,797 | 1.1 | 2.33 GHz |
| 300 | 6,708 | 6,853 | 2.2 | 2.33 GHz |
| 350 | 6,895 | 6,988 | 1.3 | 2.33 GHz |
| 400 | 6,983 | 7,084 | 1.4 | 2.33 GHz |
| 450 | 6,996 | 7,135 | 2.0 | 2.33 GHz |
| 500 | 7,151 | 7,139 | 0.2 | 2.0 GHz |

Figure 18:  Throughput Comparison of 2.0 and 2.33 GHz Xeons with 16 GB of Memory

The next three tables show power efficiency comparisons at three different memory sizes when the 2.0 GHz Xeon and 2.33 GHz Xeon were subjected to identical transaction arrival rates.

| 1 Socket, 2.0 GHz Xeon vs. 2.33 GHz Xeon, 4 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | 2.0 GHz | 2.33 GHz | 2.0 GHz | 2.33 GHz |  |  |
| Idle |  |  | 172.8 | 172.6 | 0.1 | 2.33 GHz |
| 100 | 2,407 | 2,406 | 179.4 | 179.4 | 0.0 | Equal |
| 200 | 4,814 | 4,812 | 186.8 | 186.0 | 0.4 | 2.33 GHz |
| 300 | 7,221 | 7,219 | 192.6 | 192.0 | 0.3 | 2.33 GHz |
| 400 | 9,625 | 9,627 | 198.6 | 197.2 | 0.7 | 2.33 GHz |
| 500 | 12,030 | 12,034 | 202.6 | 202.2 | 0.2 | 2.33 GHz |

Figure 19:  Power Efficiency Comparison of 2.0 GHz and 2.33 GHz Xeons with 4 GB of Memory

| 1 Socket, 2.0 GHz Xeon vs. 2.33 GHz Xeon, 8 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | 2.0 GHz | 2.33 GHz | 2.0 GHz | 2.33 GHz |  |  |
| Idle |  |  | 207.6 | 204.6 | 1.4 | 2.33 GHz |
| 100 | 2,406 | 2,406 | 220.8 | 212.6 | 3.7 | 2.33 GHz |
| 200 | 4,814 | 4,813 | 219.6 | 220.8 | 0.5 | 2.0 GHz |
| 300 | 7,221 | 7,220 | 225.4 | 224.4 | 0.4 | 2.33 GHz |
| 400 | 9,628 | 9,629 | 230.4 | 229.8 | 0.3 | 2.33 GHz |
| 500 | 12,031 | 12,031 | 234.6 | 233.8 | 0.3 | 2.33 GHz |

Figure 20:  Power Efficiency Comparison of 2.0 GHz and 2.33 GHz Xeons with 4 GB of Memory

| 1 Socket, 2.0 GHz Xeon vs. 2.33 GHz Xeon, 16 GB of Memory, 1 GB DIMMs |
| --- |
| Data Collected During 30 Minute Transaction Processing Tests |
| Active Users | Transactions Per Min. | Power Consumption in Watts | Percent Lower | Better Option |
|  | 2.0 GHz | 2.33 GHz | 2.0 GHz | 2.33 GHz |  |  |
| Idle |  |  | 270.8 | 267.8 | 1.1 | 2.33 GHz |
| 100 | 2,406 | 2,407 | 263.2 | 276.0 | 4.6 | 2.0 GHz |
| 200 | 4,814 | 4,813 | 283.4 | 282.6 | 0.3 | 2.33 GHz |
| 300 | 7,222 | 7,221 | 289.6 | 288.4 | 0.4 | 2.33 GHz |
| 400 | 9,629 | 9,625 | 295.6 | 293.4 | 0.7 | 2.33 GHz |
| 500 | 12,033 | 12,032 | 298.0 | 298.0 | 0.0 | Equal |

Figure 21:  Power Efficiency Comparison of 2.0 GHz and 2.33 GHz Xeons with 4 GB of Memory

# 7. Server Specifications

The server systems used in these tests were configured to perform the functions of both database server and application server. An Opteron and Xeon servers were selected with two CPU sockets. Either one or two quad core chips were installed depending upon the desired test configuration. Minimal changes were made to the system “tunables”. These changes are listed in Appendix “B” The following table lists the configurations of the server systems.

|  | Intel Xeon | AMD Opteron |
| --- | --- | --- |
| Processor Model | E5335/E5345, Clovertown, 65nm | 2350, Barcelona, 65nm |
| Processor Speeds | 2.0/2.33 GHz | 2.0 GHz |
| Processor L1 Cache Size | 2 x 64k/64k | 4 x 64k/64k |
| Processor L2 Cache Size | 2 x 4096k | 4 x 512k |
| Processor L3 Cache Size | n/a | 2048k |
| Bus | 1.333 MT/s Front Side Bus | 3 x 1.0 GHz HyperTransport |
| Memory Sizes | 4, 8, 16 Gigabytes | 4, 8, 16 Gigabytes |
| Memory Type | Fully Buffered DDR II – 667 MHz | DDR II – 667 MHz |
| Motherboard Brand | Supermicro | ASUS |
| Motherboard Model | X7DBE+ | KFSN4-DRE |
| Boot Drive Type | SATA II | SATA II |
| Boot Drive Brand | Western Digitial | Western Digital |
| Boot Dive Model | WD1600YD | WD1600YD |
| Boot Drive Size | 160 Gigabytes | 160 Gigabytes |
| Boot Drive Average. Seek | 8.9ms | 8.9ms |
| Boot Drive RPM | 7,200 | 7,200 |
| Data Drive Type | SATA II | SATA II |
| Data Drive Brand | Western Digital | Western Digital |
| Data Drive Model | WD1600YD | WD1600YD |
| Data Drive Size | 160 Gigabytes | 160 Gigabytes |
| Data Drive Average Seek | 8.9ms | 8.9ms |
| Data Drive RPM | 7,200 | 7,200 |
| Data Drive File System Type | Ext2 | Ext2 |
| Power Supply Brand | Ablecom | Ablecom |
| Power Supply Model | PWS-702-1R | PWS-702-1R |
| Power Supply Rating | 700 Watts | 700 Watts |
| Operating System Version | 64 bit SUSE Linux Ent Srvr 10 SP1 | 64 bit SUSE Linux Ent Srvr 10 SP1 |
| MySQL Version | 14.14, 5.1.22-rc | 14.14, 5.1.22-rc |
| Estimated System Prices |
| 1 Socket, 2.0 GHz, 4GB | $ 2,386.00 | $ 2,639.00 |
| 1 Socket, 2.0 GHz, 8GB | $ 2,643.00 | $ 2,831.00 |
| 1 Socket, 2.0 GHz, 16GB | $ 3,157.00 |  |
| 1 Socket, 2.33 GHz, 4GB | $ 2,545.00 |  |
| 1 Socket, 2.33 GHz, 8GB | $ 2,802.00 |  |
| 1 Socket, 2.33 GHz, 16GB | $ 3,316.00 |  |
| 2 Sockets, 2.0 GHz, 4GB |  | $ 3,101.00 |
| 2 Sockets, 2.0 GHz, 8GB |  | $ 3,293.00 |
| 2 Sockets, 2.0 GHz, 16GB |  | $ 3,677.00 |
| 2 Sockets, 2.33 GHz, 4GB | $ 3,100.00 |  |
| 2 Sockets, 2.33 GHz, 8GB | $ 3,357.00 |  |
| 2 Sockets, 2.33 GHz, 16GB | $ 3,871.00 |  |

Figure 22:  Server Specifications

# 8. Test Environment

These tests were conducted at the Neal Nelson &

Associates client/server testing facility.  This lab has a

test bed with 96 client machines.  The test bed is a Linux

cluster that has been configured to run under the control

of the Neal Nelson Multi-Node Remote Terminal Emulator

(RTE) software package.  In this configuration all of the

RTE client machines can be directed to perform functions

In either an independent or synchronized fashion.

In addition to the RTE client machines Opteron and Xeon

servers were used during this test sequence. The

configuration of these servers were described in section 7

of this white paper.

# 9. Test Bed Configuration

The following diagram shows the relationship between the various machines that were used in the test.

Figure 23:  Relationship of Test Bed Devices

# 10. Transaction Description

A credit card purchase was selected as the basis for this transaction test.  One common type of credit card transaction is a fuel purchase at a filling station.  This purchase consists of two steps. First the credit card is read and the fuel purchase is authorized, and second, when fuel dispensing is complete, the details of the sale are updated into a database.  In addition to the database update the transaction’s detail information is written to a transaction log file.

The transactions are submitted by simulated World Wide Web users from the RTE nodes to the Apache2 HTTP web server software that is running on the server.  The Apache2 web server, through a “.cgi” binary executable program, accesses data stored in the database tables.

The following diagram shows the information flow between the major software modules that were active during this test.

Figure 24:  Information Flow Between Major Software Components

# 11. Database

The database used by this test consists of two tables and one sequential log file.  The two tables are a “credit card” table and a “gas station” table.  The sequential file is a transaction log of the events that occur during a test run.  The layouts of the tables are listed in Appendix A.

The tables used by this test are a fixed size.  The credit card table has 200,000,000 rows and the gas station table has 75,000,000 rows.  The transaction log file is pre-allocated at a size such that it does not overflow during a test run.

# 12. Test Procedure

The test procedure consisted of the following steps:

- Configure the desired server with one or two (quad core) processors, load the operating system (SUSE Linux Enterprise Server version 10, SP 1), the database server software and the benchmark application software.

- Execute utility programs to initialize the test database and then load test data into the database.

- Re-boot the server to initialize the process table and clear the kernel disk cache.

- Reset the test database and clear the sequential transaction log file. Start background “daemon” processes to write records to the transaction log file.

- Repeat steps 3 and 4 before running the transaction test nine times with maximum throughout load levels of 100, 150, 200, 250, 300, 350, 400, 450 and 500 simultaneous users.  Repeat steps 3 and 4 before running the power efficiency test five times with transaction arrival rates of 2,400, 4,800, 7,200, 9,600 and 12,000 transactions per minute.  At each user load level transactions were presented at a steady rate for at least 30 minutes. During this thirty minute time period the server’s total power usage (in watt hours) is recorded by a “Watts Up Pro” power meter.

- Repeat steps 1 through 5 with each of the desired combinations of memory size and CPU configuration.

# 13. Conclusions

The Xeon based server configurations delivered slightly better maximum throughout than the Opteron based server configurations with the complex workloads used in these tests.

The Opteron based server configurations delivered significantly better power efficiency when systems were configured with larger numbers of memory modules.

# 14. Possible Future Tests

Repeat this test sequence 2 GB and 4 GB memory modules.

Repeat this test sequence with processors that have different clock frequencies.

# 15. Acknowledgements

We wish to gratefully acknowledge the assistance provided by MySQL, AMD and Novell/SuSE for providing resources that were used in these tests.

# 16. References

- http://www-03.ibm.com/press/us/en/pressrelease/20633.wss

- "The Rise to Power of Power: Dealing with the New Data 
Center Constraint," Jerald Murphy, Robert Frances Group. (2006)

- SPEC – Power and Performance, Design Overview, Section 2
”The SUT and its Workload”

- SPEC – Power and Performance, Design Document, Section 2.1.1
”Target Loads”

- SPEC – Power and Performance, Design Document, Section 2.2
”Transactions”

# 17. Questions and Comments

What type of assistance was provided by the vendors listed above? – Each vendor loaned us either computer equipment or software that we used during these tests.

Was Intel Invited to Participate in the Test? – Yes, Intel declined to participate.

Did anyone pay for or sponsor these tests? - No, we were not paid, directly or indirectly, by anyone to develop these benchmarks or run these tests.

Can I run these tests myself? - Yes, but they are not easy to run. These are transaction workloads that require a client/server Remote Terminal Emulation (RTE) test bed (in our case a Linux cluster), and substantial experience in database administration and RTE scripting.  These tests are comparable in complexity to the Transaction Processing Council (TPC) client/server tests.

Can you run these tests for us? - Yes, we offer both laboratory and on-site testing services. The lab tests are both quick and inexpensive.  We perform benchmarks where the test results are released to the public and we also perform tests where the results are kept under non-disclosure.

Are you available as a consultant to my company for a particular project? - Yes. Contact information is listed below.

# 18. Caution

There are many factors that affect the performance of computer systems.  In this test we have tried to isolate and measure the performance issues for a well-defined set of factors.  Individuals that review test data, such as the data contained herein, must consider all of the factors affecting performance and prepare an informed estimate of the impact of any changes that they intend to make to their configuration.

# 19. About Neal Nelson & Associates

Neal Nelson & Associates is an independent testing and consulting company founded in 1973.  It is not affiliated with any manufacturer or vendor and offers a number of products and services, including its Multinode Remote Terminal Emulator (RTE).  The firm has its primary office and a testing laboratory in the Chicago suburbs.  Neal Nelson & Associates' client list includes companies such as: FedEx, IBM, McDonald's, Northern Telecom, Sprint and major government agencies including the Internal Revenue Service, US Air Force, US Navy and US Army.

For further information contact: Neal Nelson & Associates at (847) 851-8900.

# 20. Trademarks

Trademarks that may be mentioned in this document are the property of their owners.

Appendix A:  Database Design

CREDIT CARD Table Layout

Field Name	Field Description			Comments

ccccno		variable text, 16 characters max		credit card number

ccname		variable text, 40 characters max		name on credit card

cctype		variable text, 4 characters max		credit card type

ccsccd		variable text, 8 characters max		security code

ccexmn		numeric, 2 digits			expiration month

ccexyr		numeric, 4 digits			expiration year

cctltr		numeric, 8 digits			total transactions

cctlgl		numeric, 12 digits, 3 decimals		total gallons

cctlam		numeric, 12 digits, 2 decimals		total amount

ccadr1		variable text, 40 characters max		address 1

ccadr2		variable text, 40 characters max		address 2

cccity		variable text, 32 characters max		city

ccstpv		variable text, 4 characters max		state/prov

cczpcd		variable text, 8 characters max		zip code

cczpsf		variable text, 8 characters max		zip suffix

ccprpn		variable text, 16 characters max		primary phone no.

ccprfn		variable text, 16 characters max		primary fax no.

ccprcn		variable text, 16 characters max		primary cell no.

ccprea		variable text, 40 characters max		primary email

cctxid		variable text, 32 characters max		tax i.d. number

Primary Key:  ccccno

GAS STATION Table Layout

Field Name	Field Description			Comments

gsgsid		numeric, 8 digits			gas station i.d.

gstltr		numeric, 8 digits			total transactions

gstlgl		numeric, 12 digits, 3 decimals   		total gallons

gstlam		numeric, 12 digits, 2 decimals		total amount

gsname		variable text, 40 characters max		gas station name

gsadr1		variable text, 40 characters max		address 1

gsadr2		variable text, 40 characters max		address 2

gscity		variable text, 32 characters max		city

gsstpv		variable text, 4 characters max		state/prov

gszpcd		variable text, 8 characters max		zip code

gszpsf		variable text, 8 characters max		zip suffix

gsprpn		variable text, 16 characters max		primary phone no.

gsprea		variable text, 40 characters max		primary email

gstxid		variable text, 32 characters max		tax i.d. number

pumps 1-12

gspttr[12]	numeric, 8 digits 			pump total transactions

gsptgl[12]	numeric, 12 gigits, 3 decimals		pump total gallons

gsptam[12]	numeric, 12 gigits,  decimals		pump total amount

Primary Key:  gsgsid

TRANSACTION LOG File Layout

Field Name	Field Description			Comments

tltrno		numeric, 8 digits			transaction number

tlgsid		numeric, 8 digits			gas station i.d.

tlgspm		numeric, 2 digits			gas pump i.d. (1-12)

tlccno		variable text, 16 characters		credit card number

tltcdt		numeric, 8 digits			trans completed date

tltctm		numeric, 8 digits			trans completed time

tlgaln		numeric, 8 digits, 3 decimals		gallons pumped

tltlam		numeric, 12 digits, 2 decimals		total amount of sale

Appendix B:   SUSE Linux Enterprise Server 10  Tunables

| Desired Change | File | Changes |
| --- | --- | --- |
| Disable HTTP logging | /etc/sysconfig/apache2 | Comment out APACHE_ACCESS_LOG |
| Increase number of allowed simultaneous user sessions | /etc/apache2/server_tuning.conf | change 150 to 550 |

/proc/sys/vm/dirty_expire_centisecs set to 200

/proc/sys/vm/dirty_writeback_centisecs set to 200

Appendix C:   Source Code for DBMS Queries

MySQL Queries

The SQL queries are embedded within “C” language programs. The following are portions of the C code that include the queries:

MySQL Validate Credit Card Number and Gas Station Number

ml2200:				// open database

if(mysql_init(&mysql) == NULL)

{

errrtn(5060L,"ml2200","mysql_init() error: %s"

,mysql_error(&mysql));

endjob(9);

}

if (!mysql_real_connect(&mysql,"localhost","wk0001","upwd0001",NULL,0,NULL,0))

{

errrtn(5060L,"ml2200","mysql_real_connect() error: %s"

,mysql_error(&mysql));

endjob(9);

}

wkrtcd = mysql_select_db(&mysql,"B");

if(wkrtcd != 0)		// unsuccessful

{

errrtn(5060L,"ml2200","mysql_select_db() error: %s"

,mysql_error(&mysql));

endjob(9);

}

ml2400:				// validate against credit card table

sprintf(&(query_def[0])

,"SELECT ccccno FROM cdtcrd WHERE ccccno='%16.16s'",&(tl.tlccno[0]));

wkrtcd = mysql_exec_sql(&mysql,query_def);

if (wkrtcd != 0) {

errrtn(5060L,"ml2400","error=%s"

,mysql_error(&mysql));

}

result = mysql_use_result(&mysql);

if (!result) {

errrtn(5060L,"ml2400","mysql_use_result() error: %s"

,mysql_error(&mysql));

}

mysql_free_result(result);

ml2600:				// validate against gas station table

sprintf(&(query_def[0])

,"SELECT gsgsid FROM gasstn WHERE gsgsid=%ld",tl.tlgsid);

wkrtcd = mysql_exec_sql(&mysql,query_def);

if (wkrtcd != 0) {

errrtn(5060L,"ml2600","error=%s"

,mysql_error(&mysql));

}

result = mysql_use_result(&mysql);

if (!result) {

errrtn(5060L,"ml2600","mysql_use_result() error: %s"

,mysql_error(&mysql));

}

mysql_free_result(result);

ml2800:				// close the database

mysql_close(&mysql);

MySQL Update Credit Card Number and Gas Station Number

ml3200:				// open database

if(mysql_init(&mysql) == NULL)

{

errrtn(5060L,"ml3200","mysql_init() error: %s"

,mysql_error(&mysql));

endjob(9);

}

if (!mysql_real_connect(&mysql,"localhost","wk0001","upwd0001",NULL,0,NULL,0))

{

errrtn(5060L,"ml3200","mysql_real_connect() error: %s"

,mysql_error(&mysql));

endjob(9);

}

wkrtcd = mysql_select_db(&mysql,"B");

if(wkrtcd != 0)		// unsuccessful

{

errrtn(5060L,"ml3200","mysql_select_db() error: %s"

,mysql_error(&mysql));

endjob(9);

}

wkrtcd = mysql_autocommit(&mysql,0);

if(wkrtcd != 0)		// unsuccessful

{

errrtn(5060L,"ml3200","mysql_autocommit() error: %s"

,mysql_error(&mysql));

endjob(9);

}

ml3400:				// select credit card row

sprintf(&(query_def[0])

,"SELECT cctltr, cctlgl, cctlam FROM cdtcrd WHERE ccccno='%16.16s'"

,&(tl.tlccno[0]));

wkrtcd = mysql_exec_sql(&mysql,query_def);

if (wkrtcd != 0) {

errrtn(5060L,"ml3400","error=%s"

,mysql_error(&mysql));

}

if (wkrtcd != 0) {	// 0=successful

errrtn(5060L,"ml3582","mysql_exec_sql() select error: %s"

,mysql_error(&mysql));

goto ml3600;

}

result = mysql_store_result(&mysql);

if (!result) {		// no results

errrtn(5060L,"ml3584","mysql_store_result() select error: %s"

,mysql_error(&mysql));

goto ml3600;

}

row = mysql_fetch_row(result);

ml3480:				// bring in the fields

lengths = mysql_fetch_lengths(result); // length of each field

for(i = 0; i < 3; i++)

{

sprintf(&(wkclrs[i][0])

,"%.*s", (int) lengths[i], row[i] ? row[i] : "NULL");

}

mysql_free_result(result);

sscanf(&(wkclrs[0][0]),"%ld",&(cctltr));

sscanf(&(wkclrs[1][0]),"%lf",&(cctlgl));

sscanf(&(wkclrs[2][0]),"%lf",&(cctlam));

ml3500:				// change the data fields

cctltr = cctltr + 1;

cctlgl = cctlgl + tl.tlgaln;

cctlam = cctlam + tl.tltlam;

ml3540:				// update the table

sprintf(&(query_def[0])

,"UPDATE cdtcrd SET cctltr=%ld, cctlgl=%lf, cctlam=%lf WHERE ccccno='%16.16s'"

,cctltr,cctlgl,cctlam,&(tl.tlccno[0]));

wkrtcd = mysql_exec_sql(&mysql,query_def);

if (wkrtcd != 0) {	// 0=successful

errrtn(5060L,"ml3586","mysql_exec_sql() select error: %s"

,mysql_error(&mysql));

}

ml3600:				// select gas station row

sprintf(&(query_def[0])

,"SELECT gstltr, gstlgl, gstlam, gspt%2.2d, gspg%2.2d, gspa%2.2d FROM gasstn WHERE gsgsid=%ld"

,tl.tlgspm,tl.tlgspm,tl.tlgspm,tl.tlgsid);

wkrtcd = mysql_exec_sql(&mysql,query_def);

if (wkrtcd != 0) {

errrtn(5060L,"ml3600","error=%s"

,mysql_error(&mysql));

}

if (wkrtcd != 0) {	// 0=successful

errrtn(5060L,"ml3782","mysql_exec_sql() select error: %s"

,mysql_error(&mysql));

mysql_close(&mysql);

endjob(9);

}

result = mysql_store_result(&mysql);

if (!result) {		// no results

errrtn(5060L,"ml3784","mysql_store_result() select error: %s"

,mysql_error(&mysql));

mysql_close(&mysql);

endjob(9);

}

row = mysql_fetch_row(result);

ml3680:				// bring in the fields

lengths = mysql_fetch_lengths(result); // length of each field

for(i = 0; i < 6; i++)

{

sprintf(&(wkclrs[i][0])

,"%.*s", (int) lengths[i], row[i] ? row[i] : "NULL");

}

mysql_free_result(result);

wkidm1 = tl.tlgspm - 1L;

sscanf(&(wkclrs[0][0]),"%ld",&(gstltr));

sscanf(&(wkclrs[1][0]),"%lf",&(gstlgl));

sscanf(&(wkclrs[2][0]),"%lf",&(gstlam));

sscanf(&(wkclrs[3][0]),"%ld",&(gspttr[wkidm1]));

sscanf(&(wkclrs[4][0]),"%lf",&(gsptgl[wkidm1]));

sscanf(&(wkclrs[5][0]),"%lf",&(gsptam[wkidm1]));

ml3700:				// change the data fields

gstltr = gstltr + 1;

gstlgl = gstlgl + tl.tlgaln;

gstlam = gstlam + tl.tltlam;

gspttr[wkidm1] = gspttr[wkidm1] + 1;

gsptgl[wkidm1] = gsptgl[wkidm1] + tl.tlgaln;

gsptam[wkidm1] = gsptam[wkidm1] + tl.tltlam;

ml3740:				// update the table

sprintf(&(query_def[0])

,"UPDATE gasstn SET gstltr=%ld, gstlgl=%lf, gstlam=%lf, gspt%2.2ld=%ld, gspg%2.2ld=%lf, gspa%2.2ld=%lf WHERE gsgsid=%ld"

,gstltr,gstlgl,gstlam,wkidm1+1,gspttr[wkidm1],wkidm1+1,gsptgl[wkidm1]

,wkidm1+1,gsptam[wkidm1],tl.tlgsid);

wkrtcd = mysql_exec_sql(&mysql,query_def);

if (wkrtcd != 0) {	// 0=successful

errrtn(5060L,"ml3786","mysql_exec_sql() select error: %s"

,mysql_error(&mysql));

mysql_close(&mysql);

endjob(9);

}

wkrtcd = mysql_commit(&mysql);

if (wkrtcd != 0) {	// 0=successful

errrtn(5060L,"ml3786","mysql_commit() error: %s"

,mysql_error(&mysql));

}

ml3800:				// close database

mysql_close(&mysql);

Write Records to Sequential Transaction Log File

wkdspl = smpt->smtlna * sizeof(tl); 
      wkldm1 = lseek(wktlfd,wkdspl,0); 
      if (wkldm1 != wkdspl) { 
        errrtn(9999L,"ml4000","lseek() error, file=%s, errno=%d %s" 
          ,&(tlphnm[0]),errno,strerror(errno)); 
        endjob(9); 
      } 
      wkidm2 = smpt->smtana * sizeof(tl); 
      wkidm1 = write(wktlfd,&(smpt->smtlar[0][0]),wkidm2); 
      if (wkidm1 != wkidm2) { 
        errrtn(9999L,"ml4200","write() error, file=%s, errno=%d %s" 
          ,&(tlphnm[0]),errno,strerror(errno)); 
        endjob(9); 
      } 
      smpt->smtlna = smpt->smtlna + smpt->smtana; 
      smpt->smtana = smpt->smtafa;